## Slide 1: Motion Detection with FPGAs
Group 4
Yi Qi Cao and Da Kang

## Slide 2: Overview
Video capturing through HDMI
Processing of individual frames using motion detection algorithm
Sending frames to server when motion is detected

## Slide 3: Motion Detection Algorithm
Algorithm uses “background estimators” to determine if a pixel has changed
The output is then processed to remove noise

## Slide 4: Initial Goals
Completion of custom IP that implements the motion detection algorithm
Streaming video when motion is detected
Processing and streaming at a reasonable rate; several times a second at 720p resolution

## Slide 5: Planned Block Diagram

## Slide 6: Problems
AXI lite was too slow
  A 720p frame took several seconds to process due to the amount of data transferred
Attempted to use AXI full, but unsuccessful
  Ended up rewriting the AXI lite interface to pack the data being transferred
  Also lowered resolution to 640x480
Ethernet was unexpectedly slow

## Slide 7: Final Block Diagram

## Slide 8: Project Components
Basic block design was a combination of Digilent’s HDMI I/O and Ethernet tutorials
  Custom IP was integrated into the design
Microblaze control code is partly original
  Video capture control code is from Digilent
  Ethernet streaming code is heavily modified from LwIP example, mostly original
  Custom IP control code is original

## Slide 9: Design Methodology
Managing multiple designers by assigning separate components that can be worked on in parallel
  Da Kang: implementation and testing of custom IP
  Yi Qi Cao: video streaming over Ethernet, custom IP integration, final integration

## Slide 10: Design Methodology
Incremental testing
  Create and test each part of the design separately, and incrementally combine the different parts

## Slide 11: Design Methodology
Algorithm:
  Algorithm is defined step by step; easy to translate to hardware
    More complicated functions like abs are implemented/tested in a separate module
    Each module was tested individually with a testbench
  Total integration of algorithm modules was tested by itself in a testbench, compared with a Python implementation

## Slide 12: Design Methodology
Custom IP containing algorithm was tested with a VIP testbench
Control code was tested after integration of custom IP into HDMI I/O example
Ethernet streaming tested separately and integrated at the end

## Slide 13: What We Learned
Testing is important
  In a large design, you need to know what components are working when something goes wrong
Hardware design is very slow
  A full synthesis and implementation run took close to 2 hours
  Important to test as much as possible before actually running in hardware